## Slide 1: Hydrologic analysis of the Illinois River basin in Arkansas and Oklahoma
Public Release
April 11, 2023

## Slide 2: Study partners and federal authority
U.S. Army Corps of Engineers functions as a technical arm of Congress
Everything the U.S. Army Corps of Engineers does is authorized and appropriated through legislation
Recurring authorizations exist to partner with local tribes, communities, municipalities to provide Federal assistance.
Partnership with the Cherokee Nation through the recurring “Planning Assistance to State” authority to:
  Identify the major contributing factors to increased water levels in the Illinois River Basin
  Evaluate suggestions to decrease the frequency and magnitude of flooding
  Supply data, models, information to assist in the communication of and understanding of flood risk for more localized planning entities to leverage.
  The study focuses on investigating data looking to the future and NOT full forensics on the past (circa 1990 to present)
  The study was conducted at a broad watershed level (not individual parcels) to provide a deeper understanding of conditions and to generate consistent datasets for use in planning by local level authorities.
  Corps of Engineers is NOT building dams or anything in the Illinois River Watershed.

## Slide 3: bluf
Not trying to unravel the past but trying to understand how to plan for the future
This information will be used for planning purposes- information to better understand flood risk so that local planners can divide and conquer in their area
Scenarios were simulated to understand the some best management practices at a 30,000 ft view, at a watershed scale
There is localized impact of flooding from urbanization, however we looked at it from a watershed scale, not a really small, local scale
Increase in precipitation, increase in urbanization in NW AR and land-use change along the River in OK – All contributions to flooding with the largest being the increase in precipitation

## Slide 4: Hydrology vs hydraulics
HYDROLOGY is translating precipitation to streamflow
HYDRAULICS is translating streamflow to elevation

## Slide 5: Data & Models
Statistical Models
Land-Use Model
Hydrologic Model
Hydraulic Model
Land-Use Data
Precipitation Data
Streamgage Data
Elevation Data

## Slide 6: Outline
Precipitation Trends
Land-Use Trends
Streamflow Trends
Scenarios
  Precipitation
    NOAA Atlas 14 Frequency Events
  Land use
    NLCD Historical
    Future
  Detention basins
  Riparian Buffers

## Slide 7: Gage Locations

## Slide 8: Precipitation trends

## Slide 9: Osage Creek near Elm Springs, AR
PRISM Climate Group

## Slide 10: Illinois River near Watts, OK
PRISM Climate Group

## Slide 11: Illinois River near Tahlequah, OK
PRISM Climate Group

## Slide 12: Precipitation magnitude – 24-hour
PRISM Climate Group

## Slide 13: Precipitation intensity– 24-Hour
PRISM Climate Group

## Slide 14: Land-use trends

## Slide 15: Land-Use trends
1992 Land use land cover
2001 Land use land cover
2016 Land use land cover
National Land Cover Database (NLCD)

## Slide 16: Land-Use trends
1992 = 62.2 mi2
2001 = 142.6 mi2 = 129.3% increase
2016 = 170.7 mi2 = 19.7% increase
Chart: Year
| 1992 | 2001 | 2016
Developed | 62.1962 | 142.6313 | 170.6814
Forest | 705.1342 | 778.6447 | 754.7214
Hay/Pasture | 769.2714 | 684.8605 | 654.8168
Chart: Land-use area (square miles)
| Developed | Forest | Hay/Pasture
1992 | 62.1962 | 705.1342 | 769.2714
2001 | 142.6313 | 778.6447 | 684.8605
2016 | 170.6814 | 754.7214 | 654.8168

## Slide 17: Streamflow trends

## Slide 18: Streamflow Trends
Chart: Average Annual Flow Osage Creek near Elm Springs
| 1951 | 1952 | 1953 | 1954 | 1955 | 1956 | 1957 | 1958 | 1959 | 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Average Annual flow Illinios River near Watts | 151 | 118 | 61 | 30 | 64 | 29 | 205 | 131 | 72 | 123 | 174 | 111 | 60 | 32 | 82 | 66 | 34 | 155 | 170 | 114 | 127 | 72 | 225 | 236 | 233 | 96 | 167 | 163 | 199 | 134 | 138 | 178 | 96 | 155 | 161 | 78 | 132 | 298 | 188 | 187 | 254 | 123 | 166 | 132 | 203 | 218 | 226 | 189 | 257 | 411

## Slide 19: Streamflow Trends
Chart: Average Annual flow Illinois River near Watts
Chart: Average Annual Flow Illinois River near Tahlequah

## Slide 20: Streamflow Trends
Chart: Annual Peak Flow Osage Creek near Elm Springs
| 1950 | 1951 | 1952 | 1953 | 1954 | 1955 | 1956 | 1957 | 1958 | 1959 | 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Annual Peak flow Illinios River near Watts | 22500 | 6770 | 2210 | 1820 | 4050 | 5280 | 1160 | 10800 | 2200 | 5300 | 3270 | 22500 | 2170 | 3270 | 492 | 6140 | 3270 | 684 | 8360 | 13900 | 5480 | 5910 | 3880 | 4520 | 22200 | 11600 | 5710 | 9090 | 3650 | 8140 | 6360 | 7380 | 4600 | 9320 | 8940 | 7340 | 4450 | 1690 | 18300 | 5240 | 3690 | 4680 | 15800 | 5620 | 6550 | 38000 | 5870 | 17200 | 1700 | 6660 | 23900 | 47600 | 9500 | 8670

## Slide 21: Streamflow Trends
Chart: 
Chart: Annual Peak Flow Illinois River near Tahlequah

## Slide 22
1% AEP(100-year) Flow Change Over Time
Osage Creek near Elm Springs, AR
2000
2020
2010
0
125,000
Peak flow (ft3/s)
Computed 1% AEP Flow
Confidence Limits
Observed Annual Peak Flows
Current 1% AEP Estimate

## Slide 23: 1% AEP(100-year) Flow Change Over Time
23
Illinois River near Tahlequah, OK
2000
2025
2012
0
100,000
200,000
Peak flow (ft3/s)
Computed 1% AEP Flow
Confidence Limits
Observed Annual Peak Flows
Current 1% AEP Estimate

## Slide 24: scenarios

## Slide 25: Precipitation Scenarios
Event | 24-Hour Precipitation Amount (inches)
50%AEP (2-year) | 3.76
20%AEP (5-year) | 4.71
10%AEP (10-year) | 5.48
4% AEP (25-year) | 6.57
2% AEP (50-year) | 7.45
1% AEP (100-year) | 8.37
NOAA Atlas 14 Point Precipitation Frequency Estimates
2017

## Slide 26: Land-use Scenarios
1992
2050 B2
2050 A1B
2016
2001
National Land Cover Database – USGS Earth Resources Observation and Science (EROS) Center

## Slide 27: Land-Use Scenarios
Chart: Date
| 1989.5 | 1990 | 2001 | 2004 | 2006 | 2008 | 2011 | 2013 | 2016 | 2019 | 2050 | 2050.4
 | 0.0051267 | 0.020507 | 0.023988 | 0.026046 | 0.029008 | 0.030601 | 0.031837 | 0.032745 | 0.033972 | 0.03732 | 0.070885 | 0.088983
IPCC Special Report on Emissions Scenarios (SRES) Definitions:
B2 – Emphasis is on local solutions to economic, social, and environmental sustainability; continuously increasing global population at a slower rate than other scenarios, intermediate levels of economic development, and less rapid and more diverse technological change
A1B – Very rapid economic growth, global population that peaks in mid-century and declines thereafter, and the rapid introduction of new and more efficient technologies with a “balance” across all energy sources, i.e., not relying too heavily on one particular energy source
B2
A1B
75% less developed

## Slide 28: Historical Land-use
1990
2017

## Slide 29: Historical Land-use
1990
2017

## Slide 30: Historical Land-use
1990
2017

## Slide 31: Future Land-use projections – no stormwater management considered
2050 A1B
2017
2050 B2

## Slide 32: Future Land-use projections – no stormwater management considered
2050 A1B
2050 B2
2017

## Slide 33: Future Land-use projections – no stormwater management considered
2050 A1B
2050 B2
2017

## Slide 34: Detention basins – Not recommended
2050 B2
2050 A1B
2017

## Slide 35: Riparian buffers – 1%AEP (100-Year)
2050 B2
2050 A1B
2017

## Slide 36: Riparian buffers – 1%AEP (100-Year)

## Slide 37: Take-Homes
Not trying to unravel the past but trying to understand how to plan for the future
This information will be used for planning purposes- information to better understand flood risk so that local planners can divide and conquer in their area
Scenarios were simulated to understand the some best management practices at a 30,000 ft view, at a watershed scale
There is localized impact of flooding from urbanization, however we looked at it from a watershed scale, not a really small, local scale
Increase in precipitation, increase in urbanization in NW AR and land-use change along the River in OK – All contributions to flooding with the largest being the increase in precipitation

## Slide 38
Breakout

## Slide 40: Peak Comparisons (Illinois River near Tahlequah)
Scenario/Event | Land Use | Precipitation | Peak Streamflow (cubic feet per second) | Peak Stage (elevation in feet)
2-year Frequency Event | 2016 NLCD | 2-year Frequency Event | 32,439.3 | 683.5
2-year Frequency Event w/Riparian Buffers | 2016 NLCD | 2-year Frequency Event | 27,293.6 | 682.7
5-year Frequency Event | 2016 NLCD | 5-year Frequency Event | 53,079.0 | 686.5
5-year Frequency Event w/Riparian Buffers | 2016 NLCD | 5-year Frequency Event | 41,235.3 | 685.4
10-year Frequency Event | 2016 NLCD | 10-year Frequency Event | 70,324.1 | 689.0
10-year Frequency Event w/Riparian Buffers | 2016 NLCD | 10-year Frequency Event | 53,547.5 | 687.5
25-year Frequency Event | 2016NLCD | 25-year Frequency Event | 96,216.7 | 692.1
25-year Frequency Event w/Riparian Buffers | 2016 NLCD | 25-year Frequency Event | 71,897.6 | 690.3
50-year Frequency Event | 2016 NLCD | 50-year Frequency Event | 117,495.3 | 694.4
50-year Frequency Event w/Riparian Buffers | 2016 NLCD | 50-year Frequency Event | 87,617.2 | 692.4
100-year Frequency Event | 2016 NLCD | 100-year Frequency Event | 139,794.5 | 696.9

## Slide 41: Peak Comparisons (Illinois River near Tahlequah)
Scenario/Event | Land Use | Precipitation | Peak Streamflow (cubic feet per second) | Peak Stage (elevation in feet)
100-year Frequency Event w/Riparian Buffers | 2016 NLCD | 100-year Frequency Event | 104,545.8 | 694.3
100-year Frequency Event w/B2 Land-use Scenario | 2050 SRES B2 | 100-year Frequency Event | 147,911.8 | 697.4
100-year Frequency Event w/B2 Land-use Scenario and Detention Basins | 2050 SRES B2 w/Detention Basins | 100-year Frequency Event | 107,826.7 | 693.1
100-year Frequency Event w/A1B Land-use Scenario | 2050 SRES A1B | 100-year Frequency Event | 153,017.8 | 697.7
100-year Frequency Event w/A1B Land-use Scenario and Detention Basins | 2050 SRES A1B w/Detention Basins | 100-year Frequency Event | 112,189.3 | 693.4
April 2017 Validation Event | 2016 NLCD | April 2017 Event | 110,557.7 | 694.1
0 Percent Less Developed | 0% Impervious Values | April 2017 Event | 107,678.7 | 693.7
75 Percent Less Developed | 75% 1990 Impervious Values | April 2017 Event | 108,113.9 | 693.9
B2 Land-use Scenario | 2050 SRES B2 | April 2017 Event | 116,030.2 | 694.6
B2 Land-use Scenario w/Detention Basins | 2050 SRES B2 w/Detention Basins | April 2017 Event | 89,476.5 | 691.5
A1B Land-use Scenario | 2050 SRES A1B | April 2017 Event | 118,933.1 | 694.9
A1B Land-use Scenario w/Detention Basins | 2050 SRES A1B w/Detention Basins | April 2017 Event | 92,237.7 | 691.8

## Slide 42: Osage Creek near Elm Springs, AR
PRISM Climate Group

## Slide 43: Illinois River near Watts, OK
PRISM Climate Group

## Slide 44: Illinois River near Tahlequah, OK
PRISM Climate Group